## Slide 1
Time-Division Measurement and Embedded-AI Signal Decoupling for a Soft Single-Electrode Multimodal Sensor
Bio-Robotics and Control (BiRC) Lab
Department of Mechanical Engineering
Korea University
HeeJun Moon

## Slide 2
Outline
1
I
Introduction
1.1 Background · 1.2 Limitations of Current Research · 1.3 Purpose and Significance of This Study
II
Sensor Design and Fabrication
2.1 Sensor Design · 2.2 Mechanical and Electromagnetic Characteristics · 2.3 Sensor Fabrication
III
Measurement System
3.1 Time-Division Measurement (TDM) Architecture · 3.2 Multisignal Switching PCB
IV
Signal Characterization
4.1 Experimental Setup · 4.2 Data Acquisition · 4.3 Non-Contact Mode: Strain–Proximity · 4.4 Contact Mode: Strain–Pressure · 4.5 Conductor–Dielectric · 4.6 TENG
V
Decoupling Model and Embedded Implementation for Real-Time Inference
5.1 Decoupling Model · 5.2 Embedded Implementation · 5.3 Real-Time Validation
VI
Conclusion
6.1 Summary · 6.2 Future Work

## Slide 3
I. Introduction

## Slide 4
I. Introduction
1.1 Background
A robot surface must perceive both its surroundings and its own state
3
Before contact
The approach of an object must be sensed in advance
Proximity
At contact
How hard the contact is must be known
Contact force
At all times
The body carrying the sensor itself deforms
Strain
In real interaction, however, all three stimuli act simultaneously.
→ A sensor measuring only one physical quantity has limited practical utility.
→ Distinct stimuli superimpose onto a single electrical response = signal coupling

## Slide 5
I. Introduction
1.1 Background
The case made by prior work — why each modality is needed
4
Proximity
The only means of intervening before a collision occurs
• Safe pHRI: reacting after contact is insufficient → anticipate the approach and correct the trajectory [6], [7] • Sensors over the whole arm exterior for full-surface collision avoidance [8]; quasi whole-body sensing [9] • Pre-shaping the hand before it reaches the object
Contact force
Grasp stability depends directly on the applied force
• Without tactile feedback an object is dropped, or damaged by excessive force [10] • Slip leads immediately to grasp failure unless detected and corrected quickly [11] • Proximity answers when contact occurs; force answers how hard [12]
Strain
Essential whenever the body carrying the sensor deforms
• Soft robots have effectively infinite DOF → accurate open-loop control is very difficult [13] • Proprioception is a precondition for closing the control loop [14] • Liquid-metal strain sensors enabling closed-loop soft crawling robots [15]

## Slide 6
I. Introduction
1.1 Background
Why they must be measured together, at one point — the three modalities are not independent
5
On a deforming surface, the very reference for the proximity and contact signals shifts with the deformation state.
Measured: the strain state changes the pressure sensitivity by up to 6.6× (cross-sensitivity)
At ε = 0 %, loading to 10 N → ΔR/R₀ span 3.95 %p
At ε = 30 %, loading to 9.2 N → ΔR/R₀ span 26.14 %p
→ Without knowing the strain, a given resistance change cannot be mapped to a contact force.
• Measuring the three quantities with three separate sensors does not remove this coupling.
• It merely adds the problem of registering values measured at different locations.
▶ Acquire the three signals at the very point where the coupling arises, and decouple them jointly.

## Slide 7
I. Introduction
1.2 Limitations of Current Research
Fundamental Challenge — every arrangement runs into one of three limitations
6
Array
Cross-talk · wiring · area
Wiring grows with the device count, cross-talk arises between neighbouring elements, and more area is needed [34],[35]
Stacking
Delamination · cross-talk · wiring
Wiring and cross-talk problems remain, and interlayer delamination is added as a new failure mode [36],[37]
Single-Device Decoupling
Avoids wiring, area and delamination — but…
Decoupling itself becomes hard, limiting most designs to only strain or only proximity [16]–[18],[21]
→ The wiring/cross-talk/delamination problems and the decoupling problem stem from different causes — a design that avoids one tends to inherit the other

## Slide 8
I. Introduction
1.2 Limitations of Current Research
Limitations of prior work and how this work responds
7
Prior approach
Limitation
Response in this work
Distributed rigid proximity sensors
Cannot conform to curved or deformable surfaces; wire count ∝ sensor count
A single planar, stretchable coil with a two-wire electrode
Capacitive proximity + tactile sensors
Strain and proximity appear as the same capacitance change — hard to separate
Exploits the asymmetry: L depends on (ε, d) while R depends on ε alone
Inductive soft sensors (single modality)
Use only strain or only proximity because decoupling is hard
Estimates all three simultaneously from the same coil
Hybrid integration of multiple devices
Wiring, thickness and cross-talk grow with the device count
Time-shares one device with a 1 ms TDM schedule instead of adding devices
Inductance measured with an LCR meter
Requires benchtop instrumentation; not mobile or wearable
Replaced by a 65 × 52 mm board carrying an LDC1614
PC-based AI decoupling
20–40 ms USB round trip, ±5–15 ms jitter → feedback control impossible
On-board MCU inference at 260 µs with ~2 µs spread

## Slide 9
I. Introduction
1.3 Purpose and Significance of This Study
Why a flexible, single-device sensor is needed — flexibility alone is not enough
8
① The mounting surface is curved and undergoes large deformation
An array of rigid sensors cannot conform to such a surface, and the stiffness discontinuities between elements actively impede deformation. Flexible sensors permit conformal contact and large deformation, extending to wearable applications [4],[16].
② But implementing three modalities as three devices multiplies the wiring
Wiring grows in proportion to the device count, and stacking brings added thickness, delamination risk and cross-talk between neighbouring elements [1],[5]. In large-area electronic skin, this wiring complexity has been identified as a principal bottleneck to practical deployment.
→ The approach adopted here: divide one device in time rather than multiply devices

## Slide 10
I. Introduction
1.3 Purpose and Significance of This Study
Our approach — three design decisions
9
① Single electrode
Divide one device in time rather than multiplying devices
• One EGaIn spiral coil, two wires • Device cross-talk cannot arise • Wire count stays 2 regardless of the number of modalities • Planarity and stretchability preserved
② 1 ms TDM
Apply AC excitation, DC excitation and no excitation in sequence
• AC → resonant frequency (L) • DC → voltage divider (R) • None → floating coil (TENG V) • 1 kHz acquisition, 93.9 % CPU idle
③ Embedded AI
Complete both measurement and inference inside the MCU
• Analytical inversion diverges at singularities • PC inference costs a 20–40 ms round trip • 1,413-parameter model on the STM32 • Measured 260 µs, inside the 1 ms cycle

## Slide 11
II. Sensor Design and Fabrication

## Slide 12
II. Sensor Design and Fabrication
2.1 Sensor Design
EGaIn liquid-metal planar rectangular spiral coil (120 mm initial length, 0–30 % strain)
11
A planar rectangular spiral
EGaIn liquid metal is printed onto an elastomer substrate by direct ink writing (DIW).
The conductive path survives large deformation, allowing repeated use up to 30 % strain.
One device, two roles
The coil geometry lets a single conductive trace act simultaneously as a resistive element and an inductor.

## Slide 13
II. Sensor Design and Fabrication
2.2 Mechanical and Electromagnetic Characteristics
Response signature of each stimulus
12
Stimulus
L
R_s (AC)
R_DC
V_TENG
Dominant mechanism
Stretching
↑
↑
↑
—
length ↑, section ↓ → R ↑ ; coil geometry → L ↑
Conductor approach
↓
↑
—
—
eddy-current loss → reflected impedance (attenuation)
Dielectric approach
↑
—
—
—
permittivity change / field redistribution (amplification)
Contact (charged body)
—
—
—
↑
triboelectric charge transfer
Compression (bumps)
↓*
↑
↑
—
local section ↓ ; Q ↓ → apparent L ↑
ΔL has opposite signs for conductors and dielectrics
→ not a nuisance, but information for identifying an object's electrical property

## Slide 14
II. Sensor Design and Fabrication
2.3 Sensor Fabrication
A four-step process completed by bridging and a bump array
13
Key step: bridging (routing the inner terminal out over the windings to complete a two-wire structure) · the bump array lowers the load for a 100 % ΔR/R₀ response from 210 N to 20 N (about 10×)

## Slide 15
III. Measurement System

## Slide 16
III. Measurement System
3.1 Time-Division Measurement (TDM) Architecture
AC excitation, DC excitation and no excitation cycled with a 1 ms period
15
A TIM7 interrupt starts both paths → I²C DMA (LDC1614, ~200 µs) in parallel with ADC DMA (TENG 150 µs → R 150 µs)
All transfers use DMA → no blocking wait · 93.9 % CPU idle · a fixed period prevents jitter when coupled to the AI model

## Slide 17
III. Measurement System
3.2 Multisignal Switching PCB
A dedicated six-layer board designed in EasyEDA Pro
16
• STM32G473CBT6 — Cortex-M4F 170 MHz, 128 KB flash, 32 KB SRAM
• LDC1614 — 28-bit, 1 kHz–10 MHz, I²C2 at 0x2A
• ADG734 — 4-channel analog switch, t_on 29 ns, 200 MHz BW
• 65 × 52 mm six-layer board, up to a 4-channel array
• TVS diodes protecting the TENG path

## Slide 18
IV. Signal Characterization

## Slide 19
IV. Signal Characterization
4.1 Experimental Setup
Five-axis symmetric tensile stage — an in-house symmetric tensile-and-proximity stage
18
• Four symmetric tensile axes (XA/XB/YA/YB) + an independent Z proximity axis
• 700 × 700 mm frame, Nema23 + TB6600 drivers, Arduino Uno
• 320 steps/mm, PyQt5 GUI driving the sequence
• Six-axis F/T sensor over CAN recording ground-truth force
• PC-MCU time sync + automatic is_steady tagging of accel/decel transients
Why not a commercial tensile tester?
In single-sided tension the specimen centre translates as it elongates. The proximity target must sit directly above the coil centre, so that translation becomes an error in the distance label.

## Slide 20
IV. Signal Characterization
4.2 Data Acquisition
Model inputs are always only (ΔL/L₀, ΔR/R₀); positions and forces are used solely as ground-truth labels
19
Protocol
Size
Purpose
D1
37 strain levels + continuous 50→0 mm proximity (asynchronous)
≈ 78,000 rows
Initial two-stage PINN training
D2
P1: 19 strain levels × proximity sweep P2: 13 proximity levels × strain sweep
metal 45,633 rows hand 37,116 rows
Characterizing the (ε, d) response surface
D3
Two continuous simultaneous sweeps, PC-MCU synchronized
188,232 rows → 33,450 after preprocessing
Training the proximity + strain decoupler
D4
19 strain levels × proximity-to-contact traverse with F/T recording (up to 10.1 N)
51,858 rows / 569 s
Contact physics analysis · MoE training
D5
Three on-hardware sessions (Part 1 proximity / Part 2 strain / Part 3 both)
26.7k / 34.0k / 32.6k rows
Embedded real-time validation

## Slide 21
IV. Signal Characterization
4.3 Non-Contact Mode: Strain–Proximity
The (ε, d) response surfaces — the physical reason decoupling is possible
20
Metal target
ΔR contours are essentially parallel to the distance axis → resistance depends on strain alone
ΔL contours bend sharply for d < 10 mm → at fixed strain it swings from −15.7 % to +14.5 %, changing sign
∇L and ∇R are globally linearly independent → direct evidence that decoupling is feasible

## Slide 22
IV. Signal Characterization
4.4 Contact Mode: Strain–Pressure
New physics appears when the contact modality is added — hysteresis, creep and cross-sensitivity
21
• During a constant-depth dwell, ΔL drifts a further 2.33 %p and ΔR 5.73 %p → residuals after unloading are only 0.57 %p and 0.08 %p
• So most of it is a reversible time-lag component, not permanent damage → consistent with a standard linear solid (SLS) model
▶ Exponential relaxation fit over the dwell → τ = 0.93 s (channel-wise: τ_L 1.33 s, τ_R 0.59 s; combined τ = 1.01 s)

## Slide 23
IV. Signal Characterization
4.4 Contact Mode: Strain–Pressure
Why inductance appears to rise under compression — an inversion artefact caused by the falling Q factor
22
Q = ω · (max. stored energy / energy dissipated per cycle) = X / R_s = ω L / R_s
The sensor is pressed
L ↓ , R_DC ↑ , R_eddy ↑
Q falls sharply
Q = ω L / R_s
The true resonant frequency drops
f = 1/(2π√(LC)) · √(1 − 1/Q²)
But we invert with the approximation
f ≈ 1/(2π√(LC)) , ΔL/L₀ = f₀²/f² − 1
L is reported as having increased
an artefact — not a genuine rise in inductance
No correction was applied. The learned decoupler maps (ΔL, ΔR) directly onto the target quantities, so as long as the Q dependence is consistently present in its inputs it produces correct outputs without an explicit inversion correction — a practical advantage over analytical inversion.

## Slide 24
IV. Signal Characterization
4.5 Conductor–Dielectric
How much proximity information survives depends on the target
23
Conductor (metal)
• Eddy-current loss dominates → the effective inductance drops substantially on approach
• ΔL contours bend sharply (Fig. 3a) → proximity information is strongly carried
Dielectric (hand)
• Only permittivity-driven signal amplification acts → ΔL stays positive and small
• ΔL contours are nearly vertical (Fig. 3c) → the inductance behaves essentially as a strain sensor alone
→ Proximity decoupling for dielectric targets is fundamentally harder than for conductive ones — all subsequent modelling targets the conductive case

## Slide 25
IV. Signal Characterization
4.6 TENG
An unvalidated extension — unnecessary for the gate, but retained in hardware for a reason
24
The third signal, acquired in the no-excitation slot — an event signal that peaks on charge transfer at the instant of contact (Section 2.2)
The contact gate already reaches over 98 % accuracy from ΔL and ΔR alone (Section 4.1.4) → TENG was not included as a decoupler input here
So why keep acquiring it? Two extension directions (Sections 1.3, 5)
• Contact dynamics · slip sensing — a triboelectric signal is an event signal that arises only under relative sliding motion, carrying information the steady-state L and R channels cannot [31]
• Material identification — combining the ΔL sign difference between conductors and dielectrics (Sections 2.2, 3.4) with triboelectric polarity and magnitude may extend this to broader material classification [19],[32]
Neither direction is evaluated experimentally here — both are presented only at the level of structure and physical rationale

## Slide 26
V. Decoupling Model and Embedded Implementation for Real-Time Inference

## Slide 27
V. Decoupling Model and Embedded Implementation
5.1 Decoupling Model
Why not simply invert the relations analytically? — two reasons Jacobian inversion fails
26
[ΔR, ΔL]ᵀ = J · [Δε, Δd]ᵀ → [ε, d]ᵀ = [ε₀, d₀]ᵀ + J⁻¹ · [ΔR, ΔL]ᵀ
① Truncation error
The near field is dominated by the M² term and large strain by sinh⁻¹ and ln terms → the linear approximation is valid only locally
② Singularity / loss of orthogonality
As the directions of ∇R and ∇L converge, det(J) → 0 → J⁻¹ diverges and small measurement noise is greatly amplified
Measured: direct inversion of the physics expression with the cross term → R² = 0.26 (diverging to R² = −75 near ε ≈ 0 with lower-quality data)
The problem lies in the inversion method, not in missing information → adopt a learned decoupler that performs only forward operations, so singularities cannot arise, and runs with O(1) latency
[Figure needed] The inversion's divergence trajectory near the det(J) → 0 singularity (e.g. R² vs. data quality near ε ≈ 0, as a heatmap or scatter plot) — not yet produced as a standalone figure

## Slide 28
V. Decoupling Model and Embedded Implementation
5.1 Decoupling Model
Decoupling model ① two-stage structure — the physical asymmetry, transferred directly into the architecture
27
Stage 1 : ΔR → ε̂ Stage 2 : (ΔL, ε̂) → d̂
Imposes the physical fact that resistance is a function of strain alone, as an inductive bias
Fair comparison at an equal budget (≈ 50 K parameters)
• Two-stage proximity MAE 1.783 mm (50,306 par.)
• End-to-end proximity MAE 1.827 mm (49,592 par.)
Asymmetry in the error structure
• Strain error is homoscedastic — uniform across the range
• Distance error is heteroscedastic — unstable beyond d = 10 mm
→ d ≤ 15 mm and d ≤ 10 mm are reported separately hereafter
The 978-parameter medium-deep sits at the Pareto knee — within 0.09 mm of the 50,306-parameter model

## Slide 29
V. Decoupling Model and Embedded Implementation
5.1 Decoupling Model
Decoupling model ② SLS-EMA + Gate-MoE — contact and non-contact differ in the very quantities to be produced
28
SLS-EMA: the τ = 1.01 s obtained in Section 3.3 is reduced to a causal exponential-moving-average history feature
• EMAₙ = EMAₙ₋₁ + α(xₙ − EMAₙ₋₁), α = 1 − exp(−Δt/τ) → one multiplication and one state variable; MCU cost effectively zero
• Computed from the live ΔL and ΔR alone, not from labels → the training feature is reproducible exactly on the deployed board
▶ This single feature cuts the force RMSE from 0.521 N to 0.253 N (the F/T sensor's own noise is ±0.19 N)

## Slide 30
V. Decoupling Model and Embedded Implementation
5.1 Decoupling Model
Ablation study — separating the contributions of Gate-MoE and SLS-EMA (D4, cycle-wise held-out)
29
Model
Gate acc.
Strain RMSE
Distance RMSE
Force RMSE
Param.
A: Gate-MoE + SLS-EMA
1.000
0.108 %p
0.318 mm
0.253 N
1,429
B: SLS-EMA only (unified)
—
0.288 %p
0.322 mm
0.079 mm †
1,506
C: Gate-MoE only (no history)
0.982
0.194 %p
0.410 mm
0.521 N
1,317
D: Gate-MoE + GRU
1.000
0.123 %p
0.318 mm
0.263 N
1,061
• The benefit of SLS-EMA is concentrated in force — from C to A the force RMSE falls 0.521 → 0.253 N (less than half), strain only 0.194 → 0.108 %p
• The gate-expert structure shows up from B to A — the unified model is 2.7× worse in strain RMSE (0.288 %p), because the strain response differs between regimes
• The GRU (D) ties on accuracy with only 306 parameters for the pressure expert — yet A was deployed (mature dense-layer support in X-CUBE-AI, no hidden state to carry)

## Slide 31
V. Decoupling Model and Embedded Implementation
5.2 Embedded Implementation
sklearn → ONNX → stedgeai → STM32, with on-board inference once per TDM cycle
30
Item
Two-stage INT8 (first)
medium-deep
MoE (final)
Parameters
50,306
978
1,413
Weight ROM
~52 KB
3,912 B
5.66 KB
Activation SRAM
15.3 KB
288 B
368 B
Total flash
112.5 KB (85.8 %)
~68 KB
83.5 KB (65.2 %)
Inference latency (DWT)
1,068 µs
141 µs
260 µs (p95 263 µs)
Completes within 1 ms
no
yes
yes
The latency spread is only ~2 µs → usable in a deterministic control loop
The same inference on a PC costs a 20–40 ms USB round trip with ±5–15 ms jitter → edge inference here is a requirement for real-time operation, not an optimization

## Slide 32
V. Decoupling Model and Embedded Implementation
5.2 Embedded Implementation
A failure mode visible only on hardware — offline metrics alone cannot guarantee embedded performance
31
Offline held-out gate accuracy 100.0 % → yet on hardware the gate kept reporting contact after release
Cause — a self-reinforcing loop created by the training/deployment mismatch
1
On release, the raw ΔL and ΔR change immediately
2
But the EMA stays at the pressed value for about τ ≈ 1 s
3
The gate, seeing that stale EMA, keeps reporting contact
4
Its decision never changes, so the EMA reset never triggers ↺
In training the EMA could be reset at the exact instant using the label z; the deployed board has no such ground truth.
Fix — revert the gate to a two-input form without EMA
Contact is an instantaneous physical transition with no reason to be smoothed. Offline accuracy dropped from 100.0 % to 98.2 %, but behaviour on hardware was restored. Experts A and B, where history genuinely helps regression, kept their four inputs.

## Slide 33
V. Decoupling Model and Embedded Implementation
5.3 Real-Time Validation
On-hardware real-time validation — a session separate from training, no post-hoc inference on the PC (session 0819-153948, 809 s)
32
Part 1 (0–398 s) strain held, proximity swept | Part 2 (400–730 s) proximity held, strain swept | Part 3 (from 738 s) both axes together

## Slide 34
V. Decoupling Model and Embedded Implementation
5.3 Real-Time Validation
Part-wise results — isolating the case where each axis varies alone from where both vary
33
Segment
Strain R²
Distance R²
Force R²
Part 1 — proximity only
0.981
0.940
0.430
Part 2 — strain only
0.492
−0.797
—
Part 3 — simultaneous
0.602
−2.051
—
Part 1 — all three quantities recovered well
Strain RMSE 1.37 %p · distance RMSE 2.11 mm Gate accuracy 98.3 %
Parts 2 and 3 — the distance R² goes negative
Proximity is quasi-static, so the ground-truth variance is very small. Since R² = 1 − RMSE²/Var(y), a small denominator degrades R² even for a modest absolute error. (Part 2 RMSE 6.19 mm — about 3× Part 1)
The degradation is nonetheless real: when proximity is quasi-static, the information left in the inductance falls to the noise level.

## Slide 35
VI. Conclusion

## Slide 36
VI. Conclusion
6.1 Summary
What is achievable, and what remains limited
35
Achievable• Three signals at 1 kHz through two wires — built with commercial parts on a six-layer board
• The R–ε-only asymmetry genuinely holds → outperforms an end-to-end model at equal budget
• 1,413 parameters estimate three quantities at once, with 260 µs deterministic latency
• Even viscoelasticity, which seems to obstruct modelling, improves accuracy once physically modelled
Limitations• Proximity estimation is practical only for conductive targets — dielectric targets carry a weak signal
• In quasi-static proximity segments the SNR collapses and R² turns negative
• The contact-force error approaches the F/T sensor's own noise floor (±0.19 N)
• TENG is unnecessary for the gate — other roles such as slip and material identification remain unverified

## Slide 37
VI. Conclusion
6.1 Summary
36
Three signals acquired simultaneously from one electrode
Two-wire EGaIn spiral coil · 1 ms TDM · 1 kHz · 93.9 % CPU idle
The physical basis for decoupling confirmed by measurement
R depends on ε alone, L on (ε, d) — ∇L and ∇R are globally linearly independent
Contact-regime physics identified and folded into the model
SLS viscoelasticity τ ≈ 1.0 s → causal EMA history feature; the Q-factor artefact explained
A 1,413-parameter model embedded on the STM32
On-board inference at 260 µs per TDM cycle (p95 263 µs), ~2 µs spread
On-hardware performance reported together with its limits
Part 1: strain R² 0.981 · distance R² 0.940 · gate 98 %; quasi-static degradation reported as measured

## Slide 38
VI. Conclusion
6.2 Future Work
37
(i)
Also acquire the AC equivalent series resistance R_s
Obtaining R_s in the same TDM slot completes the response signature, letting conductors and dielectrics be told apart by sign and enabling the Q-factor correction to be applied directly.
(ii)
Multi-frequency impedance measurement
Real and imaginary impedance at several frequencies would improve material discrimination and proximity estimation together, and the extra channels may ease the quasi-static problem.
(iii)
Two-dimensional strain decomposition
ΔL = f(Δl, ΔA, Δd) whereas ΔR = f(Δl) → L and R have different effective eigen-directions. The cruciform specimen and four-axis stage are already in place.
(iv)
Migration to a recurrent structure
The GRU matched the EMA-based models with 306 parameters. Verifying X-CUBE-AI's recurrent-layer support, hidden-state reset and quantization stability on this board is the next task.

## Slide 39
Thank you
Bio-Robotics and Control (BiRC) Lab
Department of Mechanical Engineering
Korea University
HeeJun Moon